## Slide 1: CSCE 313: Embedded Systems Final Project
Instructor: Jason D. Bakos

## Slide 2: Final Project
Objective:
  Begin with Lab 5
  Convert all floating-point computations to fixed-point
  Increase resolution to 1024 x 768
Use fixed-point representation for:
  z
  c
  min_x, max_x, min_y, max_y
  x2+y2 (for checking for divergence)

## Slide 3: Final Project
Both partners must demo their group’s final project
  Each group must still submit code, designs, and report on Dropbox
  Perform demo by May 3
    Until and including April 28, schedule with me

## Slide 4: Fixed-Point Review
Recall: fixed-point has fixed range
  Recall: Range of non-fixed-point n-bit integer:
    -2n-1 <= val <= 2n-1-1
  Range of signed (n,m) value:
    -2n-m-1 <= val <= 2n-m-1 – 2-m
  Need to decide where to set decimal point
    For c, [min|max]_[x|y]:
      Need to represent values from -2 to 2
      z should cover the worst case for a diverged pixel
    x2+y2 should cover the worst case for the r2 of a diverged pixel

## Slide 5: Worst Case Analysis
(2,0)
(0,2)
(1.4,1.4)
z | z2 | c | P(z) | x2+y2 | LH bits
(0,2) | (4,0) | (2,2) | (6,2) | 40 | 6
(0,2) | (4,0) | (2,2) | (6,2) | 40 | 6
(2,0) | (4,0) | (2,2) | (6,2) | 40 | 6
(2,0) | (4,0) | (2,2) | (6,2) | 40 | 6
(1.4,1.4) | (0,3.9) | (2,2) | (2,5.9) | 38.8 | 6

## Slide 6: Range and Precision
Problem:
  Multiply (32,n) val with (32,m) val => (64,n+m) val
Need a way to get 64-bit product, or we lose the upper 32 bits

## Slide 7: Multiply
10
11
11
10
A1
A0
B1
B0
Assume 4-bit registers, need 8 bit product:
x
=
A0*B0 (4b)
A0*B1 (4b)
0000
00
00
A1*B0 (4b)
0000
00
00
A1*B1 (4b)
+
+
+
11
14
154
3*2=6
3*3=9 -> 9*4=36
2*2=4 -> 4*4=16
2*3=6 -> 6*16=96
=
154

## Slide 8: Example Fixed Point Multiply
Multiply A = (32,n) val and B = (32,n) val, need C = (32,n) product:
  Declare A and B as “long”
  Declare C as “long long”
  Cast A and B as “long long”,
  C = (long long)A * (long long)B;
  Convert C from (64,2*n) to (32,n):
    Shift C n bits to the right
  Return C as int

## Slide 9: High Resolution
Goal: Increase resolution from 320x240 to 1024x768
Problems:
  Native resolution of VGA Controller is 640x480, so hardware modification is needed
  SRAM is only 512 KB, not large enough to store a higher resolution frame, so we need to move pixel buffer to SDRAM

## Slide 10: Hardware Modification
Remove SRAM interface, connect DMA controller master interface directly to SDRAM
Remove rescaler (no longer needed)
Change DMA controller settings to 1024x768
Each time you generate in SOPC Builder, must make edits to two generated Verilog files

## Slide 11: Hardware Modification
VGA_Controller_0.v, line 78 (after each generation):
parameter CW = 9;
parameter DW = 29;
parameter R_UI = 29;
parameter R_LI = 20;
parameter G_UI = 19;
parameter G_LI = 10;
parameter B_UI = 9;
parameter B_LI = 0;
/* Number of pixels */
parameter H_ACTIVE = 640;
parameter H_FRONT_PORCH = 16;
parameter H_SYNC = 96;
parameter H_BACK_PORCH = 48;
parameter H_TOTAL = 800;
/* Number of lines */
parameter V_ACTIVE = 480;
parameter V_FRONT_PORCH = 10;
parameter V_SYNC = 2;
parameter V_BACK_PORCH = 33;
parameter V_TOTAL = 525;
parameter NUMBER_OF_BITS_FOR_LINES = 10;
parameter LINE_COUNTER_INCREMENT = 10'h001;
parameter NUMBER_OF_BITS_FOR_PIXELS = 10;
parameter PIXEL_COUNTER_INCREMENT = 10'h001;
parameter CW = 9;
parameter DW = 29;
parameter R_UI = 29;
parameter R_LI = 20;
parameter G_UI = 19;
parameter G_LI = 10;
parameter B_UI = 9;
parameter B_LI = 0;
/* Number of pixels */
parameter H_ACTIVE = 1024;
parameter H_FRONT_PORCH = 24;
parameter H_SYNC = 136;
parameter H_BACK_PORCH = 160;
parameter H_TOTAL = 1344;
/* Number of lines */
parameter V_ACTIVE = 768;
parameter V_FRONT_PORCH = 3;
parameter V_SYNC = 6;
parameter V_BACK_PORCH = 29;
parameter V_TOTAL = 806;
parameter NUMBER_OF_BITS_FOR_LINES = 11;
parameter LINE_COUNTER_INCREMENT = 11'h001;
parameter NUMBER_OF_BITS_FOR_PIXELS = 11;
parameter PIXEL_COUNTER_INCREMENT = 11'h001;

## Slide 12: Hardware Modification
clocks_0.v, line 69 (after each generation):
parameter SYS_CLK_MULT = 1;
Change to:
parameter SYS_CLK_MULT = 2;
Line 174:
DE_Clock_Generator_System.clk2_divide_by = 2,
DE_Clock_Generator_System.clk2_duty_cycle = 50,
DE_Clock_Generator_System.clk2_multiply_by = 1,
Change to:
DE_Clock_Generator_System.clk2_divide_by = 7,
DE_Clock_Generator_System.clk2_duty_cycle = 50,
DE_Clock_Generator_System.clk2_multiply_by = 9,

## Slide 13: Software Modification
New pixel buffer requires 1024x768x3 = 2359296 bytes
  Allocate in the last (highest-addressed) memory:
    DE2 has 8MB, allocate at address DRAM_BASE + 8 x 220 - 2359296 = DRAM_BASE + 0x5C0000
      Leaves only 6029312 bytes for the CPUs, so allocate 1.25 MB (0x140000) to each CPU
    DE2-115 has 128 MB, allocated at address DRAM_BASE + 128 x 220 - 2359296 = DRAM_BASE + 0x7DC0000

## Slide 14: More Tips
Avoid divide: add a fixed-point constant for (1/768) and (1/1024) and multiply these
In Quartus, create a new file called lights.sdc with the following contents and add it to your project:
  create_clock CLOCK_50 -period 20
  derive_pll_clocks -create_base_clocks