## Slide 1: CSCE 313: Embedded Systems Final Project Notes
Instructor: Jason D. Bakos

## Slide 2: Final Project
Final project: report AND demonstration due by April 29
Each group must make appointment for 20 minute demonstration of their final project
  Both members must attend demo
  Otherwise, 15% penalty
Objective:
  Begin with Lab 5
  Convert all floating-point computations to fixed-point
  Increase resolution to 1024 x 768

## Slide 3: Fixed-Point
Use a fixed-point representation for:
  z
  c
  min_x, max_x, min_y, max_y
  x2+y2 (for checking for divergence)

## Slide 4: Fixed-Point Review
Recall: fixed-point has fixed range
  Recall: Range of non-fixed-point n-bit integer:
    -2n-1 <= val <= 2n-1-1
  Range of signed (n,m) value:
    -2n-m-1 <= val <= 2n-m-1 – 2-m
  Need to decide where to set decimal point
    For c, [min|max]_[x|y]:
      Need to represent values from -2 to 2
      Use (32,29) representation for [-4,4) (to include +2)
    z should cover the worst case for a diverged pixel
    x2+y2 should cover the worst case for the r2 of a diverged pixel

## Slide 5: Worst Case Analysis
(2,0)
(0,2)
(1.4,1.4)
z | c | P(z) (zx2-zy2+cx,2zxzy+cy) | LH bits | x2+y2 | LH bits
(0,2) | (0,2) | (-4,2) | 4 | 20 | 6
(0,2) | (2,0) | (-2,0) | 3 | 4 | 4
(2,0) | (0,2) | (4,2) | 4 | 20 | 6
(2,0) | (2,0) | (6,0) | 4 | 36 | 7
(1.4,1.4) | (1.4,1.4) | (1.4,5.3) | 4 | 30 | 6

## Slide 6: Range and Precision
For c, need 3 bits left of decimal: (32,29)
For z, need 4 bits left of decimal: (32,28)
For r2, need 7 bits the left of decimal: (32,25)
For row and col, need 0 to the right of the decimal: (32,0)
Problem:
  Multiply (32,n) val with (32,m) val => (64,n+m) val
Need a way to get 64-bit product, or we lose the upper 32 bits

## Slide 7: Multiply
10
11
11
10
A1
A0
B1
B0
Assume 4-bit registers, need 8 bit product:
x
=
A0*B0 (4b)
A0*B1 (4b)
0000
00
00
A1*B0 (4b)
0000
00
00
A1*B1 (4b)
+
+
+
11
14
154
3*2=6
3*3=9 -> 9*4=36
2*2=4 -> 4*4=16
2*3=6 -> 6*16=96
=
154

## Slide 8: Example Fixed Point Multiply
Multiply A = (32,n) val and B = (32,m) val, need C = (32,o) product:
  Declare A and B as “long”
  Declare C as “long long”
  Cast A and B as “long long”,
  C = (long long)A * (long long)B;
  Convert C from (64,n+m) to (32,o):
    Shift C (n+m)-o bits to the right
  Return C as int

## Slide 9: High Resolution
Goal: Increase resolution from 320x240 to 1024x768
Problems:
  Native resolution of VGA Controller is 640x480, so hardware modification is needed
  SRAM is only 512MB, not large enough to store a higher resolution frame, so we need to move pixel buffer to SDRAM

## Slide 10: Hardware Modification
Remove SRAM interface, connect DMA controller master interface directly to SDRAM
Remove rescaler (no longer needed)
Change DMA controller settings to 1024x768
Each time you generate in SOPC Builder, must make edits to two generated Verilog files

## Slide 11: Hardware Modification
VGA Controller Verilog file, line 78 (after each generation):
parameter CW = 9;
parameter DW = 29;
parameter R_UI = 29;
parameter R_LI = 20;
parameter G_UI = 19;
parameter G_LI = 10;
parameter B_UI = 9;
parameter B_LI = 0;
/* Number of pixels */
parameter H_ACTIVE = 640;
parameter H_FRONT_PORCH = 16;
parameter H_SYNC = 96;
parameter H_BACK_PORCH = 48;
parameter H_TOTAL = 800;
/* Number of lines */
parameter V_ACTIVE = 480;
parameter V_FRONT_PORCH = 10;
parameter V_SYNC = 2;
parameter V_BACK_PORCH = 33;
parameter V_TOTAL = 525;
parameter NUMBER_OF_BITS_FOR_LINES = 10;
parameter LINE_COUNTER_INCREMENT = 10'h001;
parameter NUMBER_OF_BITS_FOR_PIXELS = 10;
parameter PIXEL_COUNTER_INCREMENT = 10'h001;
parameter CW = 9;
parameter DW = 29;
parameter R_UI = 29;
parameter R_LI = 20;
parameter G_UI = 19;
parameter G_LI = 10;
parameter B_UI = 9;
parameter B_LI = 0;
/* Number of pixels */
parameter H_ACTIVE = 1024;
parameter H_FRONT_PORCH = 24;
parameter H_SYNC = 136;
parameter H_BACK_PORCH = 160;
parameter H_TOTAL = 1344;
/* Number of lines */
parameter V_ACTIVE = 768;
parameter V_FRONT_PORCH = 3;
parameter V_SYNC = 6;
parameter V_BACK_PORCH = 29;
parameter V_TOTAL = 806;
parameter NUMBER_OF_BITS_FOR_LINES = 11;
parameter LINE_COUNTER_INCREMENT = 11'h001;
parameter NUMBER_OF_BITS_FOR_PIXELS = 11;
parameter PIXEL_COUNTER_INCREMENT = 11'h001;

## Slide 12: Hardware Modification
Clocks Verilog file, line 69 (after each generation):
parameter SYS_CLK_MULT = 1;
Change to:
parameter SYS_CLK_MULT = 2;
Line 174:
DE_Clock_Generator_System.clk2_divide_by = 2,
DE_Clock_Generator_System.clk2_duty_cycle = 50,
DE_Clock_Generator_System.clk2_multiply_by = 1,
Change to:
DE_Clock_Generator_System.clk2_divide_by = 7,
DE_Clock_Generator_System.clk2_duty_cycle = 50,
DE_Clock_Generator_System.clk2_multiply_by = 9,

## Slide 13: Software Modification
New pixel buffer requires 1024x748x2 = 1572864 bytes (1.5MB)
  Should be OK with 2MB/CPU, depending on code size
Allocate in SDRAM (as a global variable):
  volatile alt_u16 pixel_buffer_memory[786432]; // 768x1024
Copy address of only one processor’s buffer to the DMA controller for F/B buffer (in main()):
  alt_up_pixel_buffer_dma_change_back_buffer_address(pixel_buffer,(unsigned int)pixel_buffer_memory);
  alt_up_pixel_buffer_dma_swap_buffers(pixel_buffer);
  while (alt_up_pixel_buffer_dma_check_swap_buffers_status(pixel_buffer));
  alt_up_pixel_buffer_dma_change_back_buffer_address(pixel_buffer,(unsigned int)pixel_buffer_memory);

## Slide 14: Software Modifications
Subsequent writes to buffer using address stored in DMA controller will write the same buffer:
  IOWR_16DIRECT(*(((alt_u32 *)VIDEO_PIXEL_BUFFER_DMA_0_BASE+1)),offset<<1,pixel_color);
  or
  alt_up_pixel_buffer_dma_draw(pixel_buffer,color,col,row);
This is because pointer is stored in global location
Note: Don’t use divide! Add a fixed-point constant for (1/768) and (1/1024) and multiply these