## Slide 1: High-Level Synthesis of a Genomic Database Search Engine
Rasha Karakchi, Jordan Bradshaw, Jason D. Bakos
This material is based upon work supported by the National Science Foundation under Grant No. 1421059.
Heterogeneous and Reconfigurable Computing Group

## Slide 2: Motivation
Genomic databases large and growing fast
NCBI BLAST widely used for database search
  Must scan perform entire database for each query
  I/O (disk) bound
Database
Database’
Downstream processing
Query
kernel

## Slide 3: Background
AACBBAV
AAC
ACB
CBB
BBA
BAV
AAC
ACB
CBB
BBA
BAV
1) Decompose query
2) Identify seeds
3) Identify High Scoring Pairs (HSPs):
BLAST Filter:
4) Look for HSPs of the same total length in each DB record
Existing FPGA implementations are direct implementations of software

## Slide 4: Our Approach
Query
Indices of likely matches
Downstream processing
Database
FPGA+DRAM
BRAM
DRAM
Disk
CPU+disk
Preprocess
Pattern match: HSPs

## Slide 5: Filter Design
 | AC | BC | CB | CV
AC | 0 | 1 | 0 | 1
BC | 0 | 0 | 0 | 0
CB | 0 | 1 | 0 | 1
CV | 0 | 0 | 0 | 0
HSP / Length | Start | Length
ACBC-8 | 0 | 1
ACCV-9 | 1 | 1
CBBC-6 | 2 | 1
CBCV-7 | 3 | 1
Record | Start
0 | 2
0 | 2
0 | 4
0 | 4
Suffix Table
Table of Contents
Index
(List of HSPs in database)
On-chip
(1 Mb)
DRAM
(160 MB)
Disk
(10X size of DB)

## Slide 6: Filter Design
Synthesized with Vivado HLS
Multiple PEs
When found, schedule access to DRAM
All PEs together synthesized as single pipeline
  Performs at WCET
Detects HSP patterns within fixed windows

## Slide 7: Results
# PEs | II | Pipeline Depth | Throughput (Mchars/s)
12 | 12 | 40 | 9.2
16 | 16 | 44 | 8.4
20 | 20 | 48 | 7.7
24 | 24 | 52 | 7.1
28 | 28 | 56 | 6.6
32 | 32 | 60 | 6.2
36 | 36 | 64 | 5.8
40 | 40 | 68 | 5.4
44 | 44 | 72 | 5.1
Threads | upper bound Thrp't. (Mc/s) | lower bound Thrp't. (Mc/s)
1 | 8.7 | 2.4
2 | 11.5 | 3.9
3 | 8.3 | 4.6
4 | 7.0 | 4.6
5 | 6.1 | 3.7
6 | 5.0 | 3.6
7 | 4.7 | 3.4
8 | 4.2 | 3.1
Faster for high-hit rate queries despite having less than half DRAM b/w
FPGA Performance
CPU Baseline Performance

## Slide 8: Thank you!
See our poster in the next poster session