## Slide 1: Test – 2 Review
Topics
  Test 2
  Y86-64 PIPE implementation
    Hazards
    Stalls
    forwarding
  Cache overview
  Virtual Memory overview
April 12, 2018
CSCE 212 Computer Architecture

## Slide 2: Test 2 Review Questions
Aggregate memory layout
RTL implementation of pop rA and rmmovq rA, D(rB)
Match code
Write Assembly |
GDB
HCL for needs_reg_ids
Forwarding
Load-use

## Slide 3: Alignment rules
Alignment rules that the compiler uses:
Align ints and floats on word boundary (divisible by four which means address in binary ends in 00, in hex 0, 4, 8, C)
Shorts (length=2) align on halfword boundary (binary address ends in 0)
Doubles Assuming m86-64 or Windows 32 bit  align doubles on double word boundary (binary address ends in 000)
For structures the entire structure is aligned to the boundary corresponding to its largest (non-array, non-structure) component
Pad to obtain alignments

## Slide 4: Aggregate memory layout m86-64
Struct { | Address in decimal | Size | Offset from start of tweet | padding
char from[18] | 1000 | 18 | 0 | 2
int age; | 1020 | 4 | 20 | 0
char gender; | 1024 | 1 | 24 | 7 (or 3 Linux IA32)
double total; | 1032 | 8 | 32 | 0
char t[18] | 1040 | 18 | 40 | 0
char last[140] | 1058 | 140 | 58 | **2 (198 200 next doubleword boundary)
 | 1200 |  |  | 

## Slide 5: Linux IA32 – doubles on word boundary
Struct { | Address in decimal | Size | Offset from start of tweet | padding
char from[18] | 1000 | 18 | 0 | 2
int age; | 1020 | 4 | 20 | 0
char gender; | 1024 | 1 | 24 | 3 Linux IA32)
double total; | 1032 | 8 | 32 | 0
char t[18] | 1040 | 18 | 40 | 0
char last[140] | 1058 | 140 | 58 | **2
 | 1200 |  |  | 

## Slide 6: RTL implementation of pop rA and rmmovq rA, D(rB)
RTL implementation (Satge Computation)
of pop rA --- Lecture 13 slide 15
and rmmovq rA, D(rB) --- Lecture 13 slide 17

## Slide 7: Stage Computation: popq
  Use ALU to increment stack pointer
  Must update two registers
    Popped value
    New stack pointer
popq rA
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valP  PC+2
Fetch
Read instruction byte
Read register byte
Compute next PC
valA  R[%rsp]
valB  R[%rsp]
Decode
Read stack pointer
Read stack pointer
valE  valB + 8
Execute
Increment stack pointer
valM  M8[valA]
Memory
Read from stack
R[%rsp]  valE
R[rA]  valM
Write
back
Update stack pointer
Write back result
PC  valP
PC update
Update PC

## Slide 8: RTL implementation rmmovq rA, D(rB)
Lecture 13 slide 15
Stage Computation: rmmovq
rmmovq rA, D(rB)
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valC  M8[PC+2]
valP  PC+10
Fetch
Read instruction byte
Read register byte
Read displacement D
Compute next PC
valA  R[rA]
valB  R[rB]
Decode
Read operand A
Read operand B
valE  valB + valC
Execute
Compute effective address
M8[valE]  valA
Memory
Write value to memory
Write
back
PC  valP
PC update
Update PC

## Slide 9: Match code
int
funasum(int n, int a[])
int i;
int sum =0;
for(i=0; i<n;==i){
sum = sum + a[i]
}
return(sum);
}

## Slide 10: Match code
int
funsum2(int n, int a[])
if (I > 2)
return(a[0]+a[1]);
else
return 0;
}

## Slide 11: Match code
int
funeven(int i, int a[])
if (i % 2 == 0)
return(a[i]);
else
return 1;
}

## Slide 12: Write Assembly |
int
funabssum(int n, int a[])
int i;
int sum =0;
for(i=0; i<n;==i){
x = a[i]
if (x<0)
x = -1*x
sum = sum + x
}
return(sum);
}
No loop C

## Slide 13: Assembly

## Slide 14: GDB
GDB - in questions b-e below assume that the breakpoint in question 'a' has just been reached.
Give a commands to set a breakpoint at func1 and then run the program.
  b func1
  r
Assuming there are at least two arguments to func1(int, char*), i.e. the first argument is an int and the second is a pointer to a string, then give commands that will print out these arguments.
  p /d $rdi
  x /1s $rsi
What command will make gdb print the next assembly instruction everytime it stops?
  display /i $rip
If a function has 9 arguments (all of length 4) give a command that will show the return address and arguments 7-9(and nothing extra).
  x /5wx $rsp
What gdb Command single steps through assembly code not stepping into functions, i.e. executing function calls atomically?
  ni

## Slide 15: 6. HCL for needs_reg_ids
bool need_regids =
icode in { IRRMOVQ, IOPQ, IPUSHQ, IPOPQ,
IIRMOVQ, IRMMOVQ, IMRMOVQ };
Lecture 13 – slide 33

## Slide 16: Y86-64 Instruction Set #2
0
1
2
3
4
5
6
7
8
9
V
D
D
Byte
pushq rA
A
0
rA
F
jXX Dest
7
fn
Dest
popq rA
B
0
rA
F
call Dest
8
0
Dest
cmovXX rA, rB
2
fn
rA
rB
irmovq V, rB
3
0
F
rB
rmmovq rA, D(rB)
4
0
rA
rB
mrmovq D(rB), rA
5
0
rA
rB
OPq rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0
rrmovq
7
0
cmovle
7
1
cmovl
7
2
cmove
7
3
cmovne
7
4
cmovge
7
5
cmovg
7
6

## Slide 17: Rest of today
Review data hazards and control hazards
Review stalls
Data forwarding
Cache overview
Virtual memory overview
Exam Spring 2016

## Slide 18: Memory Allocation Example
char big_array[1L<<24]; /* 16 MB */
char huge_array[1L<<31]; /* 2 GB */
int global = 0;
int useless() { return 0; }
int main ()
{
void *p1, *p2, *p3, *p4;
int local = 0;
p1 = malloc(1L << 28); /* 256 MB */
p2 = malloc(1L << 8); /* 256 B */
p3 = malloc(1L << 32); /* 4 GB */
p4 = malloc(1L << 8); /* 256 B */
/* Some print statements ... */
}
not drawn to scale
Where does everything go?
Stack
Text
Data
Heap
Shared
Libraries

## Slide 19: Example Memory Hierarchy
Regs
L1 cache
(SRAM)
Main memory
(DRAM)
Local secondary storage
(local disks)
Larger,
slower,
and
cheaper
(per byte)
storage
devices
Remote secondary storage
(e.g., Web servers)
Local disks hold files retrieved from disks
on remote servers
L2 cache
(SRAM)
L1 cache holds cache lines retrieved from the L2 cache.
CPU registers hold words retrieved from the L1 cache.
L2 cache holds cache lines
retrieved from L3 cache
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
and
costlier
(per byte)
storage
devices
L3 cache
(SRAM)
L3 cache holds cache lines
retrieved from main memory.
L6:
Main memory holds disk blocks retrieved from local disks.

## Slide 20: Examples of Caching in the Mem. Hierarchy
Hardware MMU
0
On-Chip TLB
Address translations
TLB
Web browser
10,000,000
Local disk
Web pages
Browser cache
Web cache
Network buffer cache
Buffer cache
Virtual Memory
L2 cache
L1 cache
Registers
Cache Type
Web pages
Parts of files
Parts of files
4-KB pages
64-byte blocks
64-byte blocks
4-8 bytes words
What is Cached?
Web proxy server
1,000,000,000
Remote server disks
OS
100
Main memory
Hardware
4
On-Chip L1
Hardware
10
On-Chip L2
NFS client
10,000,000
Local disk
Hardware + OS
100
Main memory
Compiler
0
CPU core
Managed By
Latency (cycles)
Where is it Cached?
Disk cache
Disk sectors
Disk controller
100,000
Disk firmware

## Slide 21: Intel Core i7 Cache Hierarchy
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 0
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 3
…
L3 unified cache
(shared by all cores)
Main memory
Processor package
L1 i-cache and d-cache:
  32 KB, 8-way,
  Access: 4 cycles
L2 unified cache:
  256 KB, 8-way,
  Access: 10 cycles
L3 unified cache:
  8 MB, 16-way,
  Access: 40-75 cycles
Block size: 64 bytes for all caches.

## Slide 22: General Cache Concepts
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Larger, slower, cheaper memory
viewed as partitioned into “blocks”
Data is copied in block-sized transfer units
Smaller, faster, more expensive
memory caches a subset of
the blocks
4
4
4
10
10
10

## Slide 23: Direct Mapped Cache indexing
S = 2s sets
Direct mapped: One line per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set

## Slide 24: Average Memory Access Time (AMAT)
Hit
Miss
MissRatio
Misspenalty

## Slide 25: A System Using Virtual Addressing
Used in all modern servers, laptops, and smart phones
One of the great ideas in computer science
0:
1:
M-1:
Main memory
MMU
2:
3:
4:
5:
6:
7:
Physical address
(PA)
Data word
8:
...
CPU
Virtual address
(VA)
CPU Chip
4
4100

## Slide 26: Enabling Data Structure: Page Table
A page table is an array of page table entries (PTEs) that maps virtual pages to physical pages.
  Per-process kernel data structure in DRAM
null
null
Memory resident
page table
(DRAM)
Physical memory
(DRAM)
VP 7
VP 4
Virtual memory
(disk)
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3