## Slide 1: Trends in the Infrastructure of Computing
CSCE 190: Computing in the Modern World
Jason D. Bakos
Heterogeneous and Reconfigurable Computing Group

## Slide 2: Apollo 11 vs iPhone 10
Apollo 11
  Cost: ~$200 billion
  (whole program, adjusted)
Guidance Computer (1966):
  2.048 MHz clock
  33,600 transistors
  85,000 instructions per second
iPhone 10
  Cost: ~$999
Apple A11 Bionic CPU (2017):
  2390 MHz clock (~1000X faster)
  4.3 billion transistors (125,000X more)
  57 billion instructions per second (671,000X faster)
  + Performs 600 billion neural network operations per second
  + Processes 12 million pixels per second from still image camera
  + Processes 2 million image tiles per second from record video (feature extraction, classification, and motion analysis)
  + Encodes 240 frames per second at 1920x1080 (500 million pixels per second)

## Slide 3: New Capabilities
4K video on a phone (2015)
Xbox One (2013)
Animojis (2017)
Play MP3s (but at nearly 100% CPU load) (~1996)

## Slide 4: New Capabilities
Networking (Ethernet)
  10 Megabit/s (1.25 MB/s) (1980)
  100 Megabits/s (12.5 MB/s) (1995)
  1 Gigabits/s (125 MB/s) (1999)
  10 Gigabit/s (over twisted-pair) (1.25 GB/s) (2006)
Computer memory (DRAM)
  DDR (2000): 1.6 GB/s
  DDR2 (2003): 8.5 GB/s
  DDR3 dual channel (2007): 25.6 GB/s
  DDR4 quad channel (2014): 42.7 GB/s

## Slide 5: Semiconductors
Silicon is a group IV element
Forms covalent bonds with four neighbor atoms (3D cubic crystal lattice)
Si is a poor conductor, but conduction characteristics may be altered
Add impurities/dopants replaces silicon atom in lattice
  Adds two different types of charge carriers: holes and electrons
Spacing = .543 nm
Adds holes
Creates p-type Si
Adds electrons
Creates n-type Si
Notes: 4 valence electrons: bonds with 4 neighboring atoms No charge carriers without dopants. Dopants are from group 3 (hole; p-type) or group 5 (electron; n-type) Hole and electrons are charge carriers.

## Slide 6: MOSFETs
Cut away side view
GND
VDD
- - - - - - -
+ + + + + + +
+ + + + + + + + + + + + + +
Notes: If p is grounded, no electricity from diffusion area to substrate.
Works like a switch. The gate is a capacitor (there is a glass insulator under the gate---blue in the figure); charging it draws electrons and opens a channel, opening the connection.

## Slide 7: Logic Gates
inv
NAND2
NOR2
Notes: Gates.

## Slide 8: Logic Synthesis
Behavior:
  S = A + B
  Assume A is 2 bits, B is 2 bits, C is 3 bits
A | B | C
00 (0) | 00 (0) | 000 (0)
00 (0) | 01 (1) | 001 (1)
00 (0) | 10 (2) | 010 (2)
00 (0) | 11 (3) | 011 (3)
01 (1) | 00 (0) | 001 (1)
01 (1) | 01 (1) | 010 (2)
01 (1) | 10 (2) | 011 (3)
01 (1) | 11 (3) | 100 (4)
10 (2) | 00 (0) | 010 (2)
10 (2) | 01 (1) | 011 (3)
10 (2) | 10 (2) | 100 (4)
10 (2) | 11 (3) | 101 (5)
11 (3) | 00 (0) | 011 (3)
11 (3) | 01 (1) | 100 (4)
11 (3) | 10 (2) | 101 (5)
11 (3) | 11 (3) | 110 (6)

## Slide 9: Microarchitecture
Notes: A MIPS CPU (as used in Hennessy and Patterson; in 212).

## Slide 10: Layout
3-input NAND
Notes: Polygons represent transistors (looking from the top down). Blue are wires (copper), the black (vias, vertical) connect metal to substrate; otherwise, glass in between. Grey shaded are gates. Around 180 nanometers (around 2000), the rules no longer are parametrized by lambda, because of the complicated physics at very small scale. Free MOSIS is 180 nanometers now.

## Slide 11: Synthesized and P&R’ed MIPS Architecture
Notes: P&R’ed means: Placed and Routed. MOSIS (fabrication facility at ISI at USC) would receive something like this. (core of a tiny chip here.)

## Slide 12: IC Fabrication

## Slide 13: Si Wafer
Notes: Most chips are rectangular.

## Slide 14: Improvement: Fab + Architects
90 nm
200 million transistors/chip
(2005)
65 nm
400 million transistors/chip
(2006)
Execute 2 instructions per cycle
Execute 4 instructions per cycle

## Slide 15
Moore’s Law
source: Christopher Batten, Cornell

## Slide 16: Intel Desktop Technology
Year | Processor | Transistors | Transistor Size | Performance
1982 | i286 | ~134,000 | 1.5 mm | 6 - 25 MHz
1986 | i386 | ~270,000 | 1 mm | 16 – 40 MHz
1989 | i486 | ~1 million | .8 mm | 16 - 133 MHz
1993 | Pentium | ~3 million | .6 mm | 60 - 300 MHz
1995 | Pentium Pro | ~4 million | .5 mm | 150 - 200 MHz
1997 | Pentium II | ~5 million | .35 mm | 233 - 450 MHz
1999 | Pentium III | ~10 million | .25 mm | 450 – 1400 MHz
2000 | Pentium 4 | ~50 million | 180 nm | 1.3 – 3.8 GHz
2005 | Pentium D | ~200 million | 90 nm | 2 cores/package
2006 | Core 2 | ~300 million | 65 nm | 2 cores/chip
2008 | “Nehalem” | ~800 million | 45 nm | 4 cores/chip
2010-11 | “Westmere” / “Sandy Bridge” | ~1.2 billion | 32 nm | 6 cores/chip
2012-13 | “Ivy Bridge” / ”Haswell” | ~1.4 billion | 22 nm | 8 cores/chip
2014-15 | “Broadwell” / ”Skylake” | ~2.8 billion | 14 nm | 8 cores/chip
2016-18 | “Kaby Lake” / “Coffee Lake” / “Whiskey Lake” | ~5.6 billion | 14 nm (!!!) | 8 cores/chip
2018? | “Cannon Lake” | ? | ??? | ?
End of frequency scaling
End of core scaling
End of technology scaling?

## Slide 17: Performance: Intel Desktop Peak Performance
Desktop Processor Generation | Max. Clock Speed (GHz) | Peak Integer IPC | Max. Number of Cores | Max. DRAM Bandwidth (GB/s) | Peak Floating Point (Gflop/s) | L3 cache (MB)
Core (2006) | 3.33 | 4 | 4 | 25.6 | 107 | 8
Penryn (2007) | 3.33 | 4 | 4 | 25.6 | 107 | 8
Westmere (2010) | 3.60 | 4 | 6 | 25.6 | 173 | 12
Ivy Bridge (2013) | 3.70 | 6 | 6 | 25.6 | 355 | 15
Broadwell (2015) | 3.80 | 8 | 6 | 25.6 | 365 | 30
Kaby Lake (2017) | 4.00 | 8 | 6 | 42.7 | 768 | 32

## Slide 18: Intel Desktop: Moore’s Law
Processor Generation | Transistor size (nm) | Number of transistors (millions)
Core (2006) | 65 | 105
Penryn (2007) | 45 | 228
Westmere (2010) | 32 | 800
Ivy Bridge (2013) | 22 | 1400
Broadwell (2015) | 14 | 2800
Si atom spacing = 0.5 nm
Cannon Lake (2018) | 10 | 5200
?? (2022) | 7 | 10400
?? (2025) | 5 | 20800
?? (2027) | 3 | 41600

## Slide 19: Why Learn Hardware Design?
7th gen Skylake

## Slide 20: Why Learn Hardware Design?
Apple A6
Apple A5x
Apple A7
Apple A8
Apple A9
Apple A10

## Slide 21: CPU Performance “Walls”
Power Wall
  Must maintain thermal density of ~ 1 Watt per square mm
    ~200 Watts for 200 mm2 area
  Dennard Scaling no longer in effect
    Power density increases with transistor density
    Pdynamic = ½CVDD2f

## Slide 22
Logic Levels
NMH = VOH – VIH
NML = VIL – VOL

## Slide 23: CPU Performance “Walls”
Memory Wall
  Memory usually cannot supply data to CPU fast enough
  GPUs use soldered memory for higher speed

## Slide 24: CPU Performance “Walls”
Solution: Domain-specific architecture
  Use dedicated memories to minimize data movement
  Invest resources into more arithmetic units or bigger memories
  Use the easiest form of parallelism that matches the domain
  Reduce data size and type to the simplest needed for the domain

## Slide 25: Domain-Specific Architectures
Qualcomm Snapdragon 835
  Wireless:
    Snapdragon LTE modem
    Wi-Fi module
  Processors:
    Hexagon DSP Processor
    Qualcomm Aqstic Audio Processor
    Qualcomm IZat Location Processor
    Adreno 540 GPU (DPU + VPU) Processor
    Qualcomm Spectra 180 Camera Processor
    Kryo 280 CPU (8 core ARM BigLittle)
    Qualcomm Haven Security Processor
Raspberry Pi gen1: ARM11 + 3 types of GPUs

## Slide 26: Co-Processor (GPU) Design
ALU
ALU
ALU
ALU
cache
GPU
Core 1
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
cache
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
cache
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
cache
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
cache
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
cache
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
cache
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
cache
ALU
ALU
ALU
ALU
Core 2
Core 3
Core 4
Core 5
Core 6
Core 7
Core 8
FOR i = 1 to 1000
C[i] = A[i] + B[i]
threads
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Notes: Many threads! Even 1000 in some GPUs. Each outermost loop iteration becomes a thread.

## Slide 27: Google Tensor Processing Unit

## Slide 28: Intel Crest
DNN training
16-bit fixed point
Operates on blocks of 32x32 matrices
SRAM + HBM2

## Slide 29: Pixel Visual Core
Pixel Visual Core
  Image Processing Unit
  Performs stencil operations

## Slide 30: Field Programmable Gate Arrays
FPGAs are blank slates that can be electronically reconfigured
Allows for totally customized architectures
Drawbacks:
  More difficult to program than GPUs
  10X less logic density and clock speed
Notes: Huge flexibility, must use hardware description language: very lower level, RTL, timing. In principle, much higher utilization of the hardware. Electronically (“in the field”) reconfigurable. CE students will use FPGAs in 611 and 313.

## Slide 31: Programming FPGAs
Notes: FPGA have worked very hard on compiler from C to HDL. They call it high-level synthesis. Also, used for debugging before (re-)configuring the chip.

## Slide 32: HeRC Group: Heterogeneous Computing
initialization
0.5% of run time
“hot” loop
99% of run time
clean up
0.5% of run time
49% of code
49% of code
2% of code
co-processor
Kernel speedup | Application speedup | Execution time
50 | 34 | 5.0 hours
100 | 50 | 3.3 hours
200 | 67 | 2.5 hours
500 | 83 | 2.0 hours
1000 | 91 | 1.8 hours
Combine CPUs and coprocs
Example:
  Application requires a week of CPU time
  Offload computation consumes 99% of execution time

## Slide 33: Heterogeneous Computing with FPGAs
Developed custom FPGA coprocessor architectures for:
  Computational biology
  Sparse linear algebra
  Data mining
Generally achieve 50X – 100X speedup over CPUs
Notes: Jason used these. No longer. The ones used now are very similar (2018).

## Slide 34: Heterogeneous Computing with FPGAs
Application
Overlay
(Processing Elements)
FPGA
(Logic Gates)
Hardware engineering
Design tools (compilers)

## Slide 35: Conclusions
Moore’s Law continues, but CPUs are benefitting from an increasingly lessor degree
  Power Wall
  Memory Wall
The future is in domain-specific architectures
  Hardware designers will play increasing role in introducing new capabilities
FPGA-based computing allows for fast development of new domain specific architectures