## Slide 1: Estimating Uncertain Spatial Relationships in Robotics

## Slide 2: Introduction
Need to represent and reason about spatial uncertainty
  Methods such as precision engineering, very accurate sensors, fixtures/calibration points, or multiple low-res sensors have been used to circumvent such issues
However; a problem occurs combining uncertain spatial information which is refereed to as relative information
The paper (and this presentation) presents a general solution to estimating uncertain spatial relationships regardless of the frame where the required information is

## Slide 3: The stochastic Map
What is it?
A representation that contains estimates of the special relationships, their uncertainties, and their inter-dependencies.
Spatial Relationship
This will be represented by the vector of its special variables, x
x=[x;y;r]
A probability density function can represent uncertain spatial relationship by assigning a probability to each combination of x
P(x)=f(x)dx
Estimating Probability
The first two moments of the probability distribution are estimated and defined as
Interpretation
If spatial relationship is calculated by combining evidence from many independent observations, the central limit theorem indicates that the resulting distribution will tend to be a normal distribution
Probability
Notes: Detailed knowledge of the probability distribution is usually unnecessary
Most measuring devices provide nominal value of the measured relationship
Diagonal – variances of the spatial variables
Off diagonal – covariances between the spatial variables
Not assumed to be normal, only used normal to calculate probability contours

## Slide 4: Example

## Slide 5: Estimating first 2 moments of unknown multivariate probability distribution
Linear
Y=Mx+b
Where x (nX1) is a random vector, M (rXn) is the non-random coefficient matrix, b (rX1) is a constant vector
Covariance
Covariance matrix C(y)=MC(x)M^T
Covariance between Y and Z can be found using the covariance between x and z.
Non-Linear Relationships
Since we generally won’t have the probability density function, the best approach is to estimate the non-linear function by a Taylor series expansion about the mean
Y = f(x) + FXx + ….
Fx
Fx is the matrix of patrials of f evaluated at x

## Slide 6: Non-Linear Cont.
Covariance estimates
Estimate for the mean of y
Second order Taylor series improves mean

## Slide 7: Spatial Relationships

## Slide 8: Compounding
Finding Xik
Compunding is used to calculate the resultant relationship from two given relationships
It is used to determine location after movement

## Slide 9: Inverse Relationship

## Slide 10: Composite Relationship
With compounding and the ability to reverse relationships, we can calculate the resultant of any sequence of relationships
Serviceable market
FEW
COMPETITORS
Covariance can be estimated the same way

## Slide 11: Summary
Y=g(x)
General spatial relationship among world locations
$2B
Estimated mean and covariance
$1B
Estimated relative location of one object with respect to the coordinate from of another object

## Slide 12: Building the Map

## Slide 13: Modifying the map
Entries in map may change for 2 reasons
An object moves
New spatial information is obtained
Changing the map means changing the two componets that define it
Mean
Covariance matric
Assume new information is obtained in states, k
Updates is considered to be instantaneous and estimates prior to k are denoted by (-) and new information by (+)

## Slide 14: Moving Objects
K-1 to k
No measurements of external objects are made
New state is determined by process model, f, as a function of the old state and control variables
Robot Movement
In a system of where the robot is the only dynamic element, the process model only describes its movement
Therefore, only a small part of the map needs to be changed to address this movement
Process Model

## Slide 15: New Spatial Information
There are 2 cases when adding new spatial information about objects
1. A new object is added to the scene
2. A (stochastic) constraint is added between objects already in the scene

## Slide 16: Object is added

## Slide 17: Adding Constraints
Measures the relationship of a known landmark to itself
Here the constraint Is noisy
Each constraint mathematically is the same
As long as both types of constraints come from measurements by sensors
A geometric relationship is given for some set of the object location variables
The constraint could be absolute or could also be given with a tolerance.
2 estimates in Question
Current best estimate of the relation
The new sensor information

## Slide 18: Sensors
Sensor Model
Describes how the sensor maps the spatial variables in the state vector into the sensor variables
Kalman Filter
The updated estimate is a weighted average of the two estimates where the weighted factor is proportional to the prior covariance in the state estimate and inversely proportional to the conditional covariance measurement
Given the sensor model, the conditional estimates of the sensor vales and their uncertainties, and an actual sensor measurement, the state estimate can be updated using the Kalman Filter equation

## Slide 19: Kalman Filter
The Kalman Filter generally contains a system dynamics model defined less generally than presented in the standard filter equations
If noise does not have a normal distribution, then the Kalman Filter is not optimal but produces the optimal linear estimate
If the function f and h are non-linear in the state variables, then F and H will have to be evaluated. The given formulae then represent the Extended Kalman Filter, a sub-optimal non-linear estimator.